Inglese

1. Purpose

This Procedure outlines the Personnel Protective Equipment required in the Oil

Field.

2. Scope

This Procedure covers all personnel related to Operations activities entering the

Oil Field.

3. Definition

BA (Breathing Apparatus)

This denotes a source of clean breathable air independent of the surrounding atmosphere. It

may be line-air supplied via manually operated pump or cylinders of compressed air, selfcontained

apparatus carried by the wearer or a recycled air system. Canisters, cartridge and

other forms of filter mask do not constitute Breathing Apparatus.

Drop line

A line which extends from the anchorage point and to which a lanyard or Safety harness

may be securely attached.

Fixed Anchorage

A secure point of attachment, above head height, for drop lines and lanyards.

Harness

A strap system to spread shock load over the shoulders, thighs and seat area. It shall be

used where longer free falls (in excess of 2 meters) may occur.

Lanyard

A flexible line to secure the Safety Harness to a drop line, fixed anchorage or lifeline with a

fall arrest mechanism.

Lifeline

An anchoring cable rigged between two fixed anchorage points to serve a mobile fixture

points for the attachment of Lanyards or drop lines. The purpose is to limit swing injuries by

providing a continuous overhead fixtures point as the worker moves horizontally. Important

factors to be considered include: an adequate degree of sag, the shortest practical length

possible, sufficient shock absorption and design strength proportional to the number of

workers who may use the line.

PPE (Personal Protective Equipment)

All equipment which is intended to be worn or held by a person at work and which affords

protection against one or more risks to health and safety. This includes clothing designed to

protect against adverse weather conditions.

4. Responsibility

The HSE Site Representative is the responsible to review this procedure.

All workers are responsible for implementing this Procedure.

5. Procedure

5.1 Head Protection

Head protection is to be dressed at all times in the OTU, Maintenance workshop (area

marked), Warehouse (area marked) and during any maintenance activities.

The exceptions are:

• personnel inside the offices

• personnel in a vehicle with a hard roof.

Safety helmets shall not be modified or painted. They can only be marked with the

Oil Field logo and wearer’s name title.

Safety helmets which are daily used have a realistic life of about three years and must be

replaced after that period of time, even if there are no obvious signs of damage, etc.

5.2 Work Clothing

Normal dress is Company uniform.

Specific garments are provided when handling chemicals, hydrocarbons, unusually dirty

materials, or anything which may penetrate the wearer's clothing.

Welders must dress leather moleskin jackets.

Persons working near moving machinery must dress close-fitting overalls with elastic cuffs

or short sleeves.

Under no circumstances loose or baggy clothing may be dressed.

5.3 Eye and Face Protection

Eye protection is worn at all times in the OTU, Maintenance workshop (area marked),

Warehouse (area marked) and during any maintenance activities. Appropriate eye

protection is worn during any of the following activities, regardless of the location:

• chemical handling

• dry grinding of materials with mechanical grinder

• welding or gas cutting

• scraping, chipping or cleaning the inside of a vessel

• any operation where there is a risk of flying particles or leakage of fluids.

It is essential that the correct type of eyes protection is used. When in doubt, advice shall be

sought from the HSE Staff.

5.4 Foot Protection

Foot protection is worn at all times in the OTU, Maintenance workshop (area marked),

Warehouse (area marked) and during any maintenance activities.

For activities that involve chemicals or in wet locations, special rubber boots shall be used.

Footwear with steel studs, heel plates, or exposed steel toecaps, is strictly prohibited.

If the safety shoes are damaged due to worker carelessness the subsequent substitution will

be charged to the worker.

The wearing of sandals or "sneakers" in the Oil Field is prohibited.

Visitors to the Oil Field may be exempted from the Safety footwear requirement provided they wear sound leather shoes. However, they shall not carry out any mechanical activity, or enter specifics areas or works where there is a highrisk of foot injury.

# Français

1.  Le but

Cette procédure expose brièvement l'appareil pour la protection de personnel à l'installation pétrolifère .

2.  Compétences

La procédure s'applique au personnel lié aux operations qui entrent dans l'installation pétrolifère.

3.  Definition

BA (appareil de la respiration)

ce appareil fourni une source d'air pur malgré les environs.  L'air peut etre fourni manuellement par une pompe ou sinon les bombes d'air comprimé, un appareil auto-suffisant porté par l'ouvrier ou autrement un système d'air récyclé.  Les douilles et des autre genres de masques à filtre ne font pas partie des appareils de la respiration.

Corde d'abaissement

Cela est un point d'attelage et auquelle le baudrier doit etre bien attaché.

Ancrage fixé

Un point sùr d'attelage, au dessus de la tete, pour les cordes d'abaissement et cordeaux.

Baudrier

Un fouet pour distribuer le choc par dessus des épaules, cuisses et derrière.  Il doit etre utilisé quand il y a des chutes de plus de 2 metres.

Cordeau

Une corde flexible pour fixer le baudrier de securité jusqu'à l'ancrage fixé, la corde d'abaissement ou bouée de sauvetage avec un mécanisme d'arret chute.

La bouée de sauvetage

Un cable d'attelage fixé entre deux points comme installation mobile pour attacher les cordeaux ou les cordes d'abaissement.  Le but est de limiter les blessures fournissant une installation continue pendant que l'ouvrier se déplace en direction horizontale.  Les facteur très importants de se rappeler sont:  un niveau suffisant de desserrement, la longeur plus corte qu'est possible et pratique, amortissment du choc suffisant et pussance liée au nombre d'ouvriers.

PPE (appareil de protection de corps)

Ce sont tous les appareils qui doivent etre endossés ou portés à main et qui donnent protection contre un ou plusiers risques.  Cela comprend les vetements réalisés pour proteger de mauvais temps.

4. Responsabilité

Le represenant HSE du siège est responsable de la révision de cette procédure.

Tous les ouvriers sont responsable de l'execution de cette procédure.

5. Procédure

5.1Protection de la tete

Le casque doit toujours etre mis dans l'OTU, l'atelier d'entretien (zone marquée), l'entrepot (zone marquée), et pendant les activités d'entretien.

L'exceptions sont:

le personnel dans les bureaux

le personnel à bord d'un véhicule avec la toiture dure

Les casques ne doivent pas etre modifiés ou peint.  Ils ne peuvent qu'etre marqué avec le logo de l'installation pétrolifère et le nom d'ouvrier.

Les casques qui sont utilisé tous les jours ont une durée d'environ 3 ans et ils doivent etre remplacer aprés cette période, meme si il y n'y a pas de signes évidents que il est dommagé etc.

5.2 Vetements de travail

La tenue normale de travail est l'uniforme d'entreprise.

Vetements specifiques sont fournis quand il s'agit de la manipulation des produits chimiques, hydrocarbure, matieres exceptionnellement sales ou n'importe quel produit qui peut endommager les vetements de l'ouvrier meme.

Les soudeur doivent mettre le ciré.

Les personnes qui travaillent près des machines déplaçant doivent mettre la cotte avec les poignets à fermeture elastique ou sinon les manches courtes.

En aucune façon les vetements larges ou amples doivent etre mis.

5.3 Protection des yeux et figure

Les lunettes de protection doivent etre portées tous le temp dans L'OTU(zone marquée), l'atelier d'entretien (zone marquée), l'entrepot (zone marquée), et pendant les activités d'entretien.  Les lunettes de protection adéquates sont portées pendant les activités suivantes, malgré le lieu:

La manipulation des produits chimiques

Le meulage sec de matières avec le rémouleur

La soudure ou gazcoupage

Le raclage et nettoyage à l'intérieur d'un vase

N'importe quelle operation où il y a le risque de coulage de liquides ou des fragments qui volent.

Il est trés important que les lunettes justes soient utilisés.  Dans le doute, on doit chercher conseil du personnel HSE.

5.4 La protection aux pieds

Les chaussures pour proteger les pieds sont toujours portées dans L'OTU(zone marquée), l'atelier d'entretien (zone marquée), l'entrepot (zone marquée), et pendant les activités d'entretien.

Pour les travaux avec les produit chimiques ou dans un environnement mouillé il faut mettre les bottes exprès.

Les chaussures à clou, bout renforcé d'acier découvert sont interdites.

Si les chaussures de protection sont endommagées à cause de negligence d'ouvrier le remplacement sera payé par l'ouvrier.

Les sandale ou les basket sont severemente interdites à l'installation pétrolifère.

Les invités à l'installation pétrolifère ne sont pas obligés de mettre les chaussures de protection requis à condition que ils portent les chaussures fortes en cuir.  Pourtant, ils ne doivent pas exécuter aucune activité de mechanique ou entrer dans les zones où il y a un haut risque de blessure aux pieds.